## Slide 1: NIOS软件理解
旷锦昊
2022.6.9

## Slide 2: NIOS开发
学习资料来源：
NIOS开发总结注意点V1.0
NIOS开发手记
../../../NIOS开发资料/NIOS II 开发技术实用手册--小梅哥NIOS 开发手记.pdf
../../../NIOS开发资料/05_【工具书】NIOS II 开发注意点总结V1.0.pdf

## Slide 3: 下不进去ELF文件
Onchip_rom空间分配存在问题
QSYS硬件资源不够，check-bspeditor-enable small c library&&enable reduced device drivers
需要将一些原来存到EPCS中的量存入FLASH中
在

## Slide 4
HAL 嵌入式中的概念，意思是硬件抽象层
A Hardware Abstraction Layer (HAL)

## Slide 5: Hal.enable_reduced_device_drivers
Certain drivers are compiled with reduced functionality to reduce code footprint. Not all drivers observe this setting.
The Avalon uart and Avalon jtag uart drivers switch from interrupt-driven to polled operation.
CAUTION: several device drivers are disable entirely. These include altera_avalon_cfl_flash, altera_Avalon_epcs_flash_controller, and altera_Avalon_lcd_16207 drivers. This can result in certain API to fail. You can define a symbol provided by each driver to prevent it from being removed. If true, adds -DALT_USE_SMALL_DRIVERS to ALT_CPPFLAGS in public.mk

## Slide 6: NIOS中变量存储空间
直接写存在ROM里面
通过SPI存入FLASH中
通过SPI存入EPCS中

## Slide 7
程序在alt_Avalon_spi_command处卡住
注释存参数部分 VPD VDDA等参数暂时不存入EPCS
注释 bp_table 和 tp_table 部分